# РЕФЕРАТ

# На 34 с., 22 рисунка, 2 таблицы.

BYCYCLE MOTO CROSS, ВЕЛОСИПЕДНАЯ ВТУЛКА, МЕТОД КОНЕЧНЫХ ЭЛЕМЕНТОВ, SOLDWORKS, SOLIDWORKS SIMULATION

В данной работе изложена проблема надежности велосипедной втулки, описан принцип работы втулки, проведен анализ причин возникновения поломок, вынесена гипотеза о возможных путях изменения конструкции детали с целью повышения надежности. В пакете SolidWorks созданы модели детали до и после внесения изменений в конструкцию, описан метод конечных элементов, проведены расчеты прочностных характеристик детали методом конечных элементов c помощью утилиты Simulation пакета SolidWorks.

THE ABSTRACT

34 pages, 22 pictures, 2 tables.

BYCYCLE MOTO CROSS, BYCYCLE HUB, FINITE ELEMENT MATHOD, SOLDWORKS, SOLIDWORKS SIMULATION

In this paper, the problem of the reliability of a bicycle hub is described, the principle of operation is described, the causes of faults are analyzed, a hypothesis is made about possible ways of changing the design of the part for the purpose of increasing reliability. In the SolidWorks package, the model details are created before and after making changes to the design, the finite element method is described, the strength characteristics of the part are calculated by the finite element method using the SolidWorks Simulation utility